CCD spectra reduction
Petr Škoda
Astronomický ústav AVČR
NRIAG , Helwan , Egypt 18.5.2008

---
Reduction of CCD frames
Overscan (physical, artificial)
Bias frame (zero)
Dark (time scaling – nonlinear, low SNR)
Flat (dome, twilight sky, night sky, projector)
Many ! (sqrt(n))
Cosmics (median, average, sigma-clipping, minmax )
Cosmetics – interpolation ??? !!! (vertical dispersion ? )

---
Calibrations 2m

---
Reduction – summing COP

---
Schema of COP

---
Background a sky lines

---
Sky subtraction with slit
B
A
Noise due to slit roughness
Corrected
photon
number
Signal to extract
distance
along slit
estimated background
signal uncertain
 slopes due non-parallel sides
dispersion
Do this at every wavelength!

---
Sky subtraction near bright sky lines
Poor cancellation of sky line due to:
  - Difference in line profile due to:
    - uneven slit width
    - IQ varies over field
  - Difference in line location due to:
    - tilt of slit
    - poor wavelength calibration/ solution/
Ak
Bj
Ak - Bj



object
background
object -
background


---
Errors in centroid of VRE
VRE = velocity resolution element,
the monochromatic image of the slit as recorded by the detector
Target-slit error: Centroid varies depending on position of object with respect to slit due to guiding error or movement between telescope and slit
Slit-detector error: Centroid varies due to movement between slit and detector
dispersion

---
Heliocentric correction

---
Line shift due to heliocentric corr.

---
Kottamia spectrograph

---
Kottamia spectrograph - detail

---
Bad CCD transfer - detail

---
High noise - of bad CTE

---
Detail of Halpha – 1800mm vs OES

---
 Frauenhoffer A – 1800mm vs OES