 Spectroscopy at Ondřejov 2m Telescope
Petr Škoda
Astronomical Institute ASCR
NRIAG, Helwan Egypt 18.5.2008

---
Ondřejov observatory

---
2m telescope dome
Height 21.11m
Dome diameter 20m
Mass 195t
Slit width 5m
moves on 48 wheels

---
2m telescope panorama

---
2m mirror
Primary mirror
Full diameter	208 cm
Effective diameter	200 cm
Thick	30 cm
Weight	2340 kg
Focal length	9 m
Shape	Rot. Paraboloid

---
2m telescope configurations
Primary focus
Focal length	9 m
Size of view field	21' 45''
Cassegrain focus
Effective focal length	29.16 m
Diam. of the sec. mirror	58cm
Size of view field	6' 45''
Coudé focus
Effective focal length	63.5m
Size of view field 3'

---
Coude spectrograph schema

---
Coudé room

---
Collimator
145mm diameter
4606 mm focus
off-axis parabola

---
B&L Grating 830/mm

---
Plates (1967-1992)

---
Lick Reticon 1872

---
Reticon 1872RF

---
400mm Camera
Low resolution R~6000, 5900-7200 A at Halpha
(now Cryotiger cooling)

---
LORAL 2688x512

---
Camera 700mm
SITe 2000x800 15um
R~13000 6300-6700A

---
HEROS (2000-2003)
Two channels , R~50000
3700-8500 A, gaps

---
HEROS echellegrams

---
HEROS coverage

---
OES (since 2006)

---
OES Echellegram
R~60000, 3700-11000 A, 62 orders, gaps , fringing !

---
Be stars

---
Changes of EW in Time
HD6226 : Slechta and Skoda 2004
Omi Cas : Koubsky et al. 2004

---
Zet Tau

---
V838 Mon – coude and HEROS

---
Cyg X-1 = V1357 Cyg

---
V458 Vul

---
Spectra Disentangling in Fourier Space - KOREL
HD208905: Koubsky et al. 2006

---
Echelle Spectra Problems

---
RV by Mirroring
Shift until best match of direct and flipped profile - interactive
Complicated profiles (Be)
Adjustable region of interest (wing/core)
Needs reference line position
SPEFO - Oscilloscopic
SPLAT

---
SPLAT-VO
VO Client for analysis (SSA and local files) 1D FITS IRAF WCS (CRVAL1, CDELT1)

---
SpecView 2.14.1
VO Client for analysis (SSA and local files) 1D FITS IRAF WCS (CRVAL1, CDELT1)

---
VOSpec (ESAC)
Polynomial fits
In VizieR now
Can work with SLAP!
Theoretical VO supported
Rapid development

---
FROG (Dead ?) - Period04 (no VO)